## Slide 1: Katran/XDP Acceleration Netdev conf 0x13
Real world use cases analysis
March-2019 By Rony Efraim, Amir Ancel, Mikhael Goikhman, Michael Savisko, Tal Gilboa and Noam Stolero

## Slide 2: Agenda: HW Acceleration for XDP
Using metadata prepared by the NIC HW.
Vendor agnostic by using generic Linux API like TC
Add support for XDP program to use metadata if exists
  Bypassing packet parsing (including the cache miss)
  Add rules to NIC HW to mark or drop packets

## Slide 3: ASAP2 features of ConnectX Network Adapters
Classification fields
  Ethernet Layer 2
  IP (v4 /v6)
  TCP /UDP
  Inner packet
    VXLAN / NVGRE / GENEVE fields
Flexible fields extraction by “Flexparse”
All fields mandatory by OpenFlow
Actions
  Marking (metadata)
  Steering and Forwarding
  Hair-Pin, forwarding back to the network
    Same port or 2nd port
  Header re-write
  Drop / Allow
  Counter set
  Local and Remote Host Mirroring
  Encapsulation
  De-capsulation

## Slide 4: Using NIC HW Acceleration in XDP program
App should config TC
Legacy NIC compatible
For Example :
App set action Y to flow X
  Use TC to skbedit with 0x1234 for flow X
  Config XDP program to do action Y for mark = 0x1234
App set action drop for flow Z
  Use TC to drop flow Z
  Use TC to get counter
Packets flow
eSwitch
Kernel
NIC
Hardware
User
XDP program
App
TC
Flow X skbedit mark 0x1234
Skb->mark 0x1234 DO action Y
TC HW offload
Config flow

## Slide 5: What is Katran ?
Village in Kyrgyzstan
“/bin/cat | /bin/run” with a typo
Cat running away
L4 load-balancer

## Slide 6: Katran Overview
Stateful L4 load balancing (LB)
Open source by Facebook
  Links: Open-sourcing Katran, a scalable network load balancer
      https://github.com/facebookincubator/katran

## Slide 7: Katran – Architecture
Katran has two components:
User space control plane entity
XDP based packet processing code
Shared lookup tables
between the user space and XDP
XDP program actions:
  Parsing + extract flow ID
  Key generation for new flows
  Lookup using the key to get Destination details.
  Counters update - reflecting loads to the control plane entity.
  Packet modification + Send to “Real” server

## Slide 8: Katran – Acceleration (high level)
User Space
Kernel
XDP program
LB controller Update XDP MAP Call TC mark
HW marked packets
XDP:
if (! Marked) {
Parse
Lookup flow_key
if (! flow_key) {
add to hash
Signal to user space
}
}
update stats
encapsulate + XDP_TX

## Slide 9: Katran Acceleration POC - User space app
user-space application – set-up TC rules
User-space application is responsible for the following:
  Create new maps: hw_accel_mapping, vip_map_by_id, markid_pool_mapping, hw_accel_events
  Fill-in for each forwarding CPU core markid_pool_mapping with selected range of HW marking IDs
  Consume perf events produced by XDP program via bpf_perf_event_output()
  Create TC rules for each received perf event:
  tc filter add dev [ifname] protocol ip parent ffff: flower indev [ifname] skip_sw ip_proto [tcp|udp] src_ip X.X.X.X dst_ip Y.Y.Y.Y src_port [sport] dst_port [dport] action skbedit mark [markID]
Katran modified code is on Github: https://github.com/savisko/katran/tree/xdp_off

## Slide 10: Katran Metadata Acceleration - Performance Results
46%
48%
46%
40%

## Slide 11: Katran Metadata Acceleration - Performance Results
50%
22%
12%
0%

## Slide 12: /* TODO
We learn that the improvement is less effected when number of flows is more then 10K/core
Use mark for dest id and not flow id to reduce CPU caches misses
For stats, use per flow counter from TC (HW)
Expected performance for 1M flows will be similar to 100 flows:
  Single core: ~4 Mpps
  12 cores: ~40 Mpps
*/